## Slide 1
Chapter 2 Link Layer and LANs
Our goals:
understand principles behind data link layer services:
  error detection, correction
  sharing a broadcast channel: multiple access
  link layer addressing
  reliable data transfer, flow control: later!
instantiation and implementation of various link layer technologies

## Slide 2: Chapter 2: Roadmap
  2.1 Introduction and services of Link Layer
  2.2 Error detection and correction
  2.3 Multiple access Protocols
    Channel Partitioning
    Random Access
    Taking Turns
  2.4 Addressing
  2.5 Ethernet
  2.6 Interconnections & VLAN
  2.7 PPP

## Slide 3
2.1 Introduction and services of Link Layer

## Slide 4
Some terminology:
hosts and routers are nodes
communication channels that connect adjacent nodes along communication path are links
  wired links
  wireless links
  LANs
layer-2 packet is a frame, encapsulates datagram
data-link layer has responsibility of
transferring datagram from one node
to adjacent node over a link

## Slide 5
Datagram transferred by different link protocols over different links:
  e.g., Ethernet on first link, frame relay on intermediate links, 802.11 on last link
Each link protocol provides different services
  e.g., may or may not provide RDT over link
transportation analogy
trip from Princeton to Lausanne
  limo: Princeton to JFK
  plane: JFK to Geneva
  train: Geneva to Lausanne
tourist = datagram
transport segment = communication link
transportation mode = link layer protocol
travel agent = routing algorithm

## Slide 6: Link Layer Services
Framing, link access:
  encapsulate datagram into frame, adding header, trailer
  channel access if shared medium
  “MAC” addresses used in frame headers to identify source, dest
    different from IP address!
Reliable delivery between adjacent nodes
  we learned how to do this already (chapter 3)!
  seldom used on low bit error link (fiber, some twisted pair)
  wireless links: high error rates
    Q: why both link-level and end-end reliability?

## Slide 7
Flow Control:
  pacing between adjacent sending and receiving nodes
Error Detection:
  errors caused by signal attenuation, noise.
  receiver detects presence of errors:
    signals sender for retransmission or drops frame
Error Correction:
  receiver identifies and corrects bit error(s) without resorting to retransmission
Half-duplex and full-duplex
  with half duplex, nodes at both ends of link can transmit, but not at same time

## Slide 8: Where is the link layer implemented?
in each and every host
link layer implemented in “adaptor” (aka network interface card NIC) or on a chip
  Ethernet card, 802.11 card; Ethernet chipset
  implements link, physical layer
attaches into host’s system buses
combination of hardware, software, firmware
controller
physical
transmission
cpu
memory
host
bus
(e.g., PCI)
network adapter
card
application
transport
network
link
link
physical

## Slide 9: Adaptors communicating
sending side:
  encapsulates datagram in frame
  adds error checking bits, rdt, flow control, etc.
receiving side
  looks for errors, rdt, flow control, etc.
  extracts datagram, passes to upper layer at receiving side
controller
controller
sending host
receiving host
datagram
datagram
datagram
frame

## Slide 10
2.2 Error detection
and correction

## Slide 11
EDC= Error Detection and Correction bits (redundancy)
D = Data protected by error checking, may include header fields
Error detection not 100% reliable!
  protocol may miss some errors, but rarely
  larger EDC field yields better detection and correction

## Slide 12: 1.Parity Checking
Single Bit Parity:
Detect single bit errors
Two Dimensional Bit Parity:
Detect and correct single bit errors
0
0
1
1

## Slide 13: 2.Internet checksum
Sender:
treat segment contents as sequence of 16-bit integers
checksum: addition (1’s complement sum) of segment contents
sender puts checksum value into UDP checksum field
Receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected. But maybe errors nonetheless? More later ….
Goal: detect “errors” (e.g., flipped bits) in transmitted segment (note: used at transport layer only)

## Slide 14: 3.Checksumming: Cyclic Redundancy Check
view data bits, D, as a binary number
choose r+1 bit pattern (generator), G
goal: choose r CRC bits, R, such that
  <D,R> exactly divisible by G (modulo 2)
  receiver knows G, divides <D,R> by G. If non-zero remainder: error detected!
  can detect all burst errors less than r+1 bits
widely used in practice (ATM, HDCL)

## Slide 15: CRC Example
1101010110 ← Q 商
除数 G → 110101 101000110100000 ← 2rD 被除数
110101
111011
110101
111010
110101
111110
110101
101100
110101
110010
110101
01110 ← R 余数
Want:
  D.2r XOR R = nG
equivalently:
  D.2r = nG XOR R
equivalently:
if we divide D.2r by G, want remainder R to satisfy:
R = remainder[ ]
D.2r
G

## Slide 16
国际标准已经定义了8-、16-、32-位生成多项式G；8-位CRC用于ATM头部5字节的保护；32-CRC用于大量链路层IEEE协议。
每个CRC标准能够检测少于r+1位的猝发错误和任意的奇数个比特错误……
其他检错和纠错方法不常用，故不作专门介绍
校验和通常应用于传输层，要求简单快速的软件实现方式，而CRC通常应用于链路层，可以适配器硬件实现复杂的算法。
Notes: 其他检错和纠错方法，如汉明码等在计算机网络中并不常用。
学生应该知道CRC编码解码检错算法均是在链路层网络适配器的控制芯片上硬件逻辑实现的，不是软件算法实现。

## Slide 17
2.3 Multiple access
Protocols

## Slide 18: Multiple Access Links and Protocols
Two types of “links”:
point-to-point
  PPP for dial-up access
  point-to-point link between Ethernet switch and host
broadcast (shared wire or medium)
  traditional Ethernet
  upstream HFC
  802.11 wireless LAN
shared wire (e.g.,
cabled Ethernet)
shared RF
(e.g., 802.11 WiFi)
shared RF
(satellite)
humans at a
cocktail party
(shared air, acoustical)

## Slide 19: Multiple Access protocols
single shared broadcast channel
two or more simultaneous transmissions by nodes: interference
  collision if node receives two or more signals at the same time
multiple access protocol
distributed algorithm that determines how nodes share channel, i.e., determine when node can transmit
communication about channel sharing must use channel itself!
  no out-of-band channel for coordination

## Slide 20: Ideal Mulitple Access Protocol
Broadcast channel of rate R bps
1. When one node wants to transmit, it can send at rate R.
2. When M nodes want to transmit, each can send at average rate R/M
3. Fully decentralized:
  no special node to coordinate transmissions
  no synchronization of clocks, slots
4. Simple

## Slide 21: MAC Protocols: a taxonomy
Three broad classes:
Channel Partitioning
  divide channel into smaller “pieces” (time slots, frequency, code)
  allocate piece to node for exclusive use
Random Access
  channel not divided, allow collisions
  “recover” from collisions
“Taking turns”
  Nodes take turns, but nodes with more to send can take longer turns

## Slide 22: Channel Partitioning MAC protocols: TDMA
TDMA: time division multiple access
access to channel in "rounds"
each station gets fixed length slot (length = pkt trans time) in each round
unused slots go idle
example: 6-station LAN, 1,3,4 have pkt, slots 2,5,6 idle
1
3
4
1
3
4
6-slot
frame
6-slot
frame

## Slide 23: Channel Partitioning MAC protocols: FDMA
FDMA: frequency division multiple access
channel spectrum divided into frequency bands
each station assigned fixed frequency band
unused transmission time in frequency bands go idle
example: 6-station LAN, 1,3,4 have pkt, frequency bands 2,5,6 idle
frequency bands
time
FDM cable

## Slide 24: Random Access Protocols
When node has packet to send
  transmit at full channel data rate R.
  no a priori coordination among nodes
two or more transmitting nodes ➜ “collision”,
random access MAC protocol specifies:
  how to detect collisions
  how to recover from collisions (e.g., via delayed retransmissions)
Examples of random access MAC protocols:
  slotted ALOHA
  ALOHA
  CSMA, CSMA/CD, CSMA/CA

## Slide 25: Slotted ALOHA
Assumptions
all frames same size
time is divided into equal size slots, time to transmit 1 frame
nodes start to transmit frames only at beginning of slots
nodes are synchronized
if 2 or more nodes transmit in slot, all nodes detect collision
Operation
when node obtains fresh frame, it transmits in next slot
if no collision, node can send new frame in next slot
if collision, node retransmits frame in each subsequent slot with prob. p until success

## Slide 26
Pros
single active node can continuously transmit at full rate of channel
highly decentralized: only slots in nodes need to be in sync
simple
Cons
collisions, wasting slots
idle slots
nodes may be able to detect collision in less than time to transmit packet
clock synchronization
1
1
1
1
2
3
2
2
3
3
node 1
node 2
node 3
C
C
C
S
S
S
E
E
E

## Slide 27: Slotted Aloha efficiency
Suppose N nodes with many frames to send, each transmits in slot with probability p
prob that node 1 has success in a slot = p(1-p)N-1
prob that any node has a success = Np(1-p)N-1
For max efficiency with N nodes, find p* that maximizes Np(1-p)N-1
For many nodes, take limit of Np*(1-p*)N-1 as N goes to infinity, gives 1/e = .37
Efficiency: long-run fraction of successful slots (many nodes, each with many frames to send)
At best: channel
used for useful
transmissions 37%
of time!

## Slide 28: Pure (unslotted) ALOHA
unslotted Aloha: simpler, no synchronization
when frame first arrives
  transmit immediately
collision probability increases:
  frame sent at t0 collides with other frames sent in [t0-1,t0+1]

## Slide 29: Pure Aloha efficiency
P(success by given node) = P(node transmits) .
P(no other node transmits in [p0-1,p0] .
P(no other node transmits in [p0-1,p0]
= p . (1-p)N-1 . (1-p)N-1
= p . (1-p)2(N-1)
… choosing optimum p and then letting n -> ∞
= 1/(2e) = .18
Even worse !

## Slide 30: CSMA (Carrier Sense Multiple Access)
CSMA: listen before transmit:
If channel sensed idle: transmit entire frame
If channel sensed busy, defer transmission
Human analogy: don’t interrupt others!

## Slide 31: CSMA collisions
collisions can still occur:
propagation delay means
two nodes may not hear
each other’s transmission
collision:
entire packet transmission
time wasted
spatial layout of nodes
note:
role of distance & propagation delay in determining collision probability

## Slide 32: CSMA/CD (Collision Detection)
CSMA/CD: carrier sensing, deferral as in CSMA
  collisions detected within short time
  colliding transmissions aborted, reducing channel wastage
collision detection:
  easy in wired LANs: measure signal strengths, compare transmitted, received signals
  difficult in wireless LANs: receiver shut off while transmitting
human analogy: the polite conversationalist

## Slide 33: CSMA/CD collision detection

## Slide 34
数据帧
干扰信号

TJ
A
B
TB
t

B 发送数据
A 检测
到冲突
开始冲突
信
道
占
用
时
间
A 发送数据
B也能够检测到冲突，并立即停止发送数据帧，接着就发送干扰信号。这里为了简单起见，只画出A发送干扰信号的情况。

## Slide 35: “Taking Turns” MAC protocols
channel partitioning MAC protocols:
  share channel efficiently and fairly at high load
  inefficient at low load: delay in channel access, 1/N bandwidth allocated even if only 1 active node!
Random access MAC protocols
  efficient at low load: single node can fully utilize channel
  high load: collision overhead
“taking turns” protocols
  look for best of both worlds!

## Slide 36: “Taking turns” MAC protocols
polling:
master node “invites” slave nodes to transmit in turn
typically used with “dumb” slave devices
concerns:
  polling overhead
  latency
  single point of failure (master)
master
slaves
poll
data
data

## Slide 37: “Taking turns” MAC protocols
token passing:
control token passed from one node to next sequentially.
token message
concerns:
  token overhead
  latency
  single point of failure (token)
T
data
(nothing
to send)
T

## Slide 38
cable headend
CMTS
ISP
cable modem
termination system
multiple 40Mbps downstream (broadcast) channels
  single CMTS transmits into channels
multiple 30 Mbps upstream channels
  multiple access: all users contend for certain upstream channel time slots (others assigned)
Cable access network
cable
modem
splitter
…
…
Internet frames, TV channels, control transmitted
downstream at different frequencies
upstream Internet frames, TV control, transmitted
upstream at different frequencies in time slots

## Slide 39
DOCSIS: data over cable service interface spec
FDM over upstream, downstream frequency channels
TDM upstream: some slots assigned, some have contention
  downstream MAP frame: assigns upstream slots
  request for upstream slots (and data) transmitted random access (binary backoff) in selected slots
MAP frame for
Interval [t1, t2]
Residences with cable modems
Downstream channel i
Upstream channel j
t1
t2
Assigned minislots containing cable modem
upstream data frames
Minislots containing
minislots request frames
cable headend
CMTS
Cable access network

## Slide 40: Summary of MAC protocols
channel partitioning, by time, frequency or code
  Time Division, Frequency Division
random access (dynamic),
  ALOHA, S-ALOHA, CSMA, CSMA/CD
  carrier sensing: easy in some technologies (wire), hard in others (wireless)
  CSMA/CD used in Ethernet
  CSMA/CA used in 802.11
taking turns
  polling from central site, token passing
  Bluetooth, FDDI, token ring

## Slide 41: LAN technologies
Data link layer so far:
  services, error detection/correction, multiple access
Next: LAN technologies
  addressing
  Ethernet
  hubs, switches
  PPP

## Slide 42
匹配电阻
集线器
干线耦合器
总线网
星形网
树形网
环形网

## Slide 43
2.4 Addressing

## Slide 44: MAC Addresses and ARP
32-bit IP address:
  network-layer address for interface
  used for layer 3 (network layer) forwarding
MAC (or LAN or physical or Ethernet) address:
  function: used ‘locally” to get frame from one interface to another physically-connected interface (same network, in IP-addressing sense)
  48 bit MAC address (for most LANs) burned in NIC ROM, also sometimes software settable
  e.g.: 1A-2F-BB-76-09-AD

## Slide 45: LAN Addresses and ARP
Each adapter on LAN has unique LAN address
Broadcast address =
FF-FF-FF-FF-FF-FF
adapter
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
(wired or
wireless)

## Slide 46
MAC address allocation administered by IEEE
manufacturer buys portion of MAC address space (to assure uniqueness)
Analogy:
(a) MAC address: like Social Security Number
(b) IP address: like postal address
MAC flat address ➜ portability
  can move LAN card from one LAN to another
IP hierarchical address NOT portable
  depends on IP subnet to which node is attached

## Slide 47: ARP: Address Resolution Protocol
Each IP node (Host, Router) on LAN has ARP table
ARP Table: IP/MAC address mappings for some LAN nodes
< IP address; MAC address; TTL>
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)
Question: how to determine
MAC address of B
knowing B’s IP address?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.23
137.196.7.78
137.196.7.14
137.196.7.88

## Slide 48: ARP protocol: Same LAN (network)
A wants to send datagram to B, and B’s MAC address not in A’s ARP table.
A broadcasts ARP query packet, containing B's IP address
  Dest MAC address = FF-FF-FF-FF-FF-FF
  all machines on LAN receive ARP query
B receives ARP packet, replies to A with its (B's) MAC address
  frame sent to A’s MAC address (unicast)
A caches (saves) IP-to-MAC address pair in its ARP table until information becomes old (times out)
  soft state: information that times out (goes away) unless refreshed
ARP is “plug-and-play”:
  nodes create their ARP tables without intervention from net administrator

## Slide 49: Addressing: routing to another LAN
walkthrough: send datagram from A to B via R
  focus on addressing – at IP (datagram) and MAC layer (frame)
  assume A knows B’s IP address
  assume A knows IP address of first hop router, R (how?)
  assume A knows R’s MAC address (how?)
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B

## Slide 50: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
A creates IP datagram with IP source A, destination B
A creates link-layer frame with R's MAC address as destination address, frame contains A-to-B IP datagram
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B

## Slide 51: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
frame sent from A to R
IP
Eth
Phy
frame received at R, datagram removed, passed up to IP
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
IP src: 111.111.111.111
IP dest: 222.222.222.222
IP src: 111.111.111.111
IP dest: 222.222.222.222

## Slide 52: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP src: 111.111.111.111
IP dest: 222.222.222.222
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as destination address, frame contains A-to-B IP datagram
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy

## Slide 53: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as destination address, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy

## Slide 54: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as dest, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 55
2.5 Ethernet

## Slide 56: 2.5 Ethernet
“dominant” wired LAN technology:
cheap $20 for 100Mbs!
first widely used LAN technology
Simpler, cheaper than token LANs and ATM
Kept up with speed race: 10 Mbps – 10 Gbps
Metcalfe’s Ethernet
sketch

## Slide 57: Ethernet: physical topology
bus: popular through mid 90s
  all nodes in same collision domain (can collide with each other)
star: prevails today
  active switch in center
  each “spoke” runs a (separate) Ethernet protocol (nodes do not collide with each other)
switch
bus: coaxial cable
star

## Slide 58: Ethernet Frame Structure
Sending adapter encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
Preamble:
7 bytes with pattern 10101010 followed by one byte with pattern 10101011
used to synchronize receiver, sender clock rates
dest.
address
source
address
data (payload)
CRC
preamble
type

## Slide 59
Addresses: 6 byte source, destination MAC addresses
  if adapter receives frame with matching destination address, or with broadcast address (eg ARP packet), it passes data in frame to net-layer protocol
  otherwise, adapter discards frame
Type: indicates the higher layer protocol (mostly IP but others may be supported such as Novell IPX and AppleTalk)
CRC: checked at receiver, if error is detected, the frame is simply dropped
dest.
address
source
address
data (payload)
CRC
preamble
type

## Slide 60: 以太网 V2 的 MAC 帧格式
MAC 帧
物理层
MAC 层
IP 层
目的地址
源地址
类型
数 据
FCS
6
6
2
4
字节
46 ~ 1500
IP 数据报
数据字段 46 ~ 1500 字节
数据字段的正式名称是 MAC 客户数据字段
最小长度 64 字节  18 字节的首部和尾部 = 数据字段的最小长度

## Slide 61: 无效的 MAC 帧
帧的长度不是整数个字节；
用收到的帧检验序列 FCS 查出有差错；
数据字段的长度不在 46 ~ 1500 字节之间。
有效的 MAC 帧长度为 64 ~ 1518 字节之间。
对于检查出的无效 MAC 帧就简单地丢弃。以太网不负责重传丢弃的帧。

## Slide 62: Unreliable, connectionless service
connectionless: no handshaking between sending and receiving NICs
unreliable: receiving NIC doesn't send acks or nacks to sending NIC
  data in dropped frames recovered only if initial sender uses higher layer rdt (e.g., TCP), otherwise dropped data lost
Ethernet’s MAC protocol: unslotted CSMA/CD with binary backoff

## Slide 63: Ethernet uses CSMA/CD
No slots
adapter doesn’t transmit if it senses that some other adapter is transmitting, that is, carrier sense
transmitting adapter aborts when it senses that another adapter is transmitting, that is, collision detection
Before attempting a retransmission, adapter waits a random time, that is, random access

## Slide 64
Jam Signal: make sure all other transmitters are aware of collision; 48 bits
Bit time: .1 microsec for 10 Mbps Ethernet ; for K=1023, wait time is about 50 msec
Exponential Backoff:
Goal: adapt retransmission attempts to estimated current load
  heavy load: random wait will be longer
first collision: choose K from {0,1}; delay is K· 512 bit transmission times
after second collision: choose K from {0,1,2,3}…
after ten collisions, choose K from {0,1,2,3,4,…,1023}

## Slide 65: Ethernet CSMA/CD algorithm
1. NIC receives datagram from network layer, creates frame
2. If NIC senses channel idle, starts frame transmission. If NIC senses channel busy, waits until channel idle, then transmits.
3. If NIC transmits entire frame without detecting another transmission, NIC is done with frame !
4. If NIC detects another transmission while transmitting, aborts and sends jam signal
5. After aborting, NIC enters binary (exponential) backoff:
  after mth collision, NIC chooses K at random from {0,1,2, …, 2m-1}. NIC waits K·512 bit times, returns to Step 2
  longer backoff interval with more collisions

## Slide 66: CSMA/CD efficiency
Tprop = max prop between 2 nodes in LAN
ttrans = time to transmit max-size frame
Efficiency goes to 1 as tprop goes to 0
Goes to 1 as ttrans goes to infinity
Much better than ALOHA, but still decentralized, simple, and cheap

## Slide 67: 载波监听多点接入/碰撞检测 CSMA/CD
CSMA/CD 表示 Carrier Sense Multiple Access with Collision Detection。
“多点接入”表示许多计算机以多点接入的方式连接在一根总线上。
“载波监听”是指每一个站在发送数据之前先要检测一下总线上是否有其他计算机在发送数据，如果有，则暂时不要发送数据，以免发生碰撞。
总线上并没有什么“载波”。因此， “载波监听”就是用电子技术检测总线上有没有其他计算机发送的数据信号。

## Slide 68: 碰撞检测
“碰撞检测”就是计算机边发送数据边检测信道上的信号电压大小。
当几个站同时在总线上发送数据时，总线上的信号电压摆动值将会增大（互相叠加）。
当一个站检测到的信号电压摆动值超过一定的门限值时，就认为总线上至少有两个站同时在发送数据，表明产生了碰撞。
所谓“碰撞”就是发生了冲突。因此“碰撞检测”也称为“冲突检测”。

## Slide 69: 检测到碰撞后
在发生碰撞时，总线上传输的信号产生了严重的失真，无法从中恢复出有用的信息来。
每一个正在发送数据的站，一旦发现总线上出现了碰撞，就要立即停止发送，免得继续浪费网络资源，然后等待一段随机时间后再次发送。

## Slide 70: 电磁波在总线上的有限传播速率的影响
当某个站监听到总线是空闲时，也可能总线并非真正是空闲的。
A 向 B 发出的信息，要经过一定的时间后才能传送到 B。
B 若在 A 发送的信息到达 B 之前发送自己的帧(因为这时 B 的载波监听检测不到 A 所发送的信息)，则必然要在某个时间和 A 发送的帧发生碰撞。
碰撞的结果是两个帧都变得无用。

## Slide 71
1 km
A
B
t
碰撞
t = 2  
A 检测到发生碰撞
t =   
B 发送数据
B 检测到发生碰撞
t = 
t = 0
单程端到端
传播时延记为
传播时延对载波监听的影响

## Slide 72
1 km
A
B
t
碰撞
t =   
B 检测到信道空闲
发送数据
t =    / 2
发生碰撞
t = 2  
A 检测到发生碰撞
t =   
B 发送数据
B 检测到发生碰撞
t = 
A
B
A
B
A
B
t = 0
A 检测到
信道空闲
发送数据
A
B
t = 0
t = 
B 检测到发生碰撞
停止发送
STOP
t = 2  
A 检测到
发生碰撞
STOP
A
B
单程端到端
传播时延记为

## Slide 73: 重要特性
使用 CSMA/CD 协议的以太网不能进行全双工通信而只能进行双向交替通信（半双工通信）。
每个站在发送数据之后的一小段时间内，存在着遭遇碰撞的可能性。
这种发送的不确定性使整个以太网的平均通信量远小于以太网的最高数据率。

## Slide 74: 争用期
最先发送数据帧的站，在发送数据帧后至多经过时间 2 （两倍的端到端往返时延）就可知道发送的数据帧是否遭受了碰撞。
以太网的端到端往返时延 2 称为争用期，或碰撞窗口。
经过争用期这段时间还没有检测到碰撞，才能肯定这次发送不会发生碰撞。

## Slide 75: 二进制指数类型退避算法 (truncated binary exponential type)
发生碰撞的站在停止发送数据后，要推迟（退避）一个随机时间才能再发送数据。
  确定基本退避时间，一般是取为争用期 2。
  定义重传次数 k ，k  10，即
  k = Min[重传次数, 10]
  从整数集合[0,1,…, (2k 1)]中随机地取出一个数，记为 r。重传所需的时延就是 r 倍的基本退避时间。
  当重传达 16 次仍不能成功时即丢弃该帧，并向高层报告。

## Slide 76: 争用期的长度
以太网取 51.2 s 为争用期的长度。
对于 10 Mb/s 以太网，在争用期内可发送512 bit，即 64 字节。
以太网在发送数据时，若前 64 字节没有发生冲突，则后续的数据就不会发生冲突。

## Slide 77: 最短有效帧长
如果发生冲突，就一定是在发送的前 64 字节之内。
由于一检测到冲突就立即中止发送，这时已经发送出去的数据一定小于 64 字节。
以太网规定了最短有效帧长为 64 字节，凡长度小于 64 字节的帧都是由于冲突而异常中止的无效帧。

## Slide 78: 强化碰撞
当发送数据的站一旦发现发生了碰撞时：
  立即停止发送数据；
  再继续发送若干比特的人为干扰信号(jamming signal)，以便让所有用户都知道现在已经发生了碰撞。

## Slide 79: 人为干扰信号
数据帧
干扰信号

TJ
A
B
TB
t

B 发送数据
A 检测
到冲突
开始冲突
信
道
占
用
时
间
A 发送数据
B 也能够检测到冲突，并立即停止发送数据帧，接着就发送干扰信号。这里为了简单起见，只画出 A 发送干扰信号的情况。

## Slide 80: 帧间最小间隔
帧间最小间隔为 9.6 s，相当于 96 bit 的发送时间。
一个站在检测到总线开始空闲后，还要等待 9.6 s 才能再次发送数据。
这样做是为了使刚刚收到数据帧的站的接收缓存来得及清理，做好接收下一帧的准备。

## Slide 81: 10BaseT and 100BaseT
10/100 Mbps rate; latter called “fast ethernet”
T stands for Twisted Pair
Nodes connect to a hub: “star topology”; 100 m max distance between nodes and hub
twisted pair
hub

## Slide 82: Gbit Ethernet
uses standard Ethernet frame format
allows for point-to-point links and shared broadcast channels
in shared mode, CSMA/CD is used; short distances between nodes required for efficiency
uses hubs, called here “Buffered Distributors”
Full-Duplex at 1 Gbps for point-to-point links
10 Gbps now !

## Slide 83
2.6 Interconnections:
Hubs and switches

## Slide 84
互连局域网网段的网络设备
中继器: （物理层）
转换器：信号转换的中继器
  如光电转换, 10base-2转换到10BaseT
集线器: （物理层）
  集线器是中继器的一种形式，也称为多端口中继器。
交换机: （链路层）
  交换机是网桥的一种形式，也称为多端口网桥。
Notes: 局域网如何连接网络设备，以及局域网又如何互联？
网络互联涉及到物理层物理网段的互联，链路层逻辑网段的互联，以及网络层IP子网的互联。
后面我们将陆续给出局域网互联设备简介。先介绍物理层物理网段的互联—中继器、信号转换器、集线器，链路层逻辑网段的互联– 交换机（或叫网桥）。

## Slide 85: Hubs
Hubs are essentially physical-layer repeaters:
  bits coming from one link go out all other links
  at the same rate
  no frame buffering
  no CSMA/CD at hub: adapters detect collisions
  provides net management functionality
twisted pair
hub

## Slide 86: The working principle of HUB
A、peer to peer

## Slide 87: B、点到多点通信
集
线
器
整形放大
The function of HUB：
Forwarding
整形放大

## Slide 88: Manchester encoding
Used in 10BaseT
Each bit has a transition
Allows clocks in sending and receiving nodes to synchronize to each other
  no need for a centralized, global clock among nodes!
Hey, this is physical-layer stuff!

## Slide 89: Interconnecting with hubs
Backbone hub interconnects LAN segments
Extends max distance between nodes
But individual segment collision domains become one large collision domain
Can’t interconnect 10BaseT & 100BaseT
hub
hub
hub
hub

## Slide 90
A
B
①
②
③
④
⑤
5-4-3-2-1 Rule
Notes: 5：允许5个网段，每网段最大长度100米。
4：在同一信道上允许连接4个中继器或集线器。
3：在其中的三个网段上可以增加节点。
2：在另外两个网段上，除做中继器链路外，不能接任何节点。
1：上述将组建一个大型的冲突域，最大站点数1024，网络直径达2500米。

## Slide 91: Ethernet switch
link-layer device: takes an active role
  store, forward Ethernet frames
  examine incoming frame’s MAC address, selectively forward frame to one-or-more outgoing links when frame is to be forwarded on segment, uses CSMA/CD to access segment
transparent
  hosts are unaware of presence of switches
plug-and-play, self-learning
  switches do not need to be configured

## Slide 92: Switch: multiple simultaneous transmissions
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link, but no collisions; full duplex
  each link is its own collision domain
switching: A-to-A’ and B-to-B’ can transmit simultaneously, without collisions
switch with six interfaces
(1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6

## Slide 93: Switch forwarding table
Q: how does switch know A’ reachable via interface 4, B’ reachable via interface 5?
switch with six interfaces
(1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
A: each switch has a switch table, each entry:
  (MAC address of host, interface to reach host, time stamp)
  looks like a routing table!
Q: how are entries created, maintained in switch table?
  something like a routing protocol?

## Slide 94: Switch: self-learning
A
A’
B
B’
C
C’
1
2
3
4
5
6
switch learns which hosts can be reached through which interfaces
  when frame received, switch “learns” location of sender: incoming LAN segment
  records sender/location pair in switch table
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60

## Slide 95: Switch: frame filtering/forwarding
when frame received at switch: 1. record incoming link, MAC address of sending host
  2. index switch table using MAC destination address
  3. if entry found for destination then {
  if destination on segment from which frame arrived then drop frame
  else forward frame on interface indicated by entry
  }
  else flood /* forward on all interfaces except arriving interface */

## Slide 96: Self-learning, forwarding: example
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
switch table
(initially empty)
A
1
60
A A’
A A’
A A’
A A’
A A’
frame destination, A’, location unknown:
flood
A’ A
destination A location known:
A’
4
60
selectively send
on just one link

## Slide 97: Interconnecting switches
self-learning switches can be connected together:
Q: sending from A to G - how does S1 know to forward frame destined to G via S4 and S3?
A: self learning! (works exactly the same as in single-switch case!)
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 98: Self-learning multi-switch example
Suppose C sends frame to I, I responds to C
Q: show switch tables and packet forwarding in S1, S2, S3, S4
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 99: Institutional network
to external
network
router
IP subnet
mail server
web server

## Slide 100: Switches vs. routers
both are store-and-forward:
routers: network-layer devices (examine network-layer headers)
switches: link-layer devices (examine link-layer headers)
both have forwarding tables:
routers: compute tables using routing algorithms, IP addresses
switches: learn forwarding table using flooding, learning, MAC addresses
application
transport
network
link
physical
network
link
physical
link
physical
switch
datagram
application
transport
network
link
physical
frame
frame
frame
datagram

## Slide 101: Summary comparison

## Slide 102: VLANs: motivation
consider:
CS user moves office to EE, but wants connect to CS switch?
single broadcast domain:
  all layer-2 broadcast traffic (ARP, DHCP, unknown location of destination MAC address) must cross entire LAN
  security/privacy, efficiency issues
Computer
Science
Electrical
Engineering
Computer
Engineering

## Slide 103: VLANs
port-based VLAN: switch ports grouped (by switch management software) so that single physical switch ……
switch(es) supporting VLAN capabilities can be configured to define multiple virtual LANS over single physical LAN infrastructure.
Virtual Local
Area Network
1
8
9
16
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
Electrical Engineering
(VLAN ports 1-8)
…
1
8
2
7
9
16
10
15
…
Computer Science
(VLAN ports 9-16)
… operates as multiple virtual switches

## Slide 104: Port-based VLAN
1
8
9
16
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
traffic isolation: frames to/from ports 1-8 can only reach ports 1-8
  can also define VLAN based on MAC addresses of endpoints, rather than switch port
dynamic membership: ports can be dynamically assigned among VLANs
router
forwarding between VLANS: done via routing (just as with separate switches)
  in practice vendors sell combined switches plus routers

## Slide 105: VLANS spanning multiple switches
trunk port: carries frames between VLANS defined over multiple physical switches
  frames forwarded within VLAN between switches can’t be vanilla 802.1 frames (must carry VLAN ID info)
  802.1q protocol adds/removed additional header fields for frames forwarded between trunk ports
1
8
9
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
2
7
3
Ports 2,3,5 belong to EE VLAN
Ports 4,6,7,8 belong to CS VLAN
5
4
6
8
16
1

## Slide 106
type
2-byte Tag Protocol Identifier
(value: 81-00)
Tag Control Information (12 bit VLAN ID field,
3 bit priority field like IP TOS)
Recomputed
CRC
802.1Q VLAN frame format
802.1 frame
802.1Q frame
dest.
address
source
address
data (payload)
CRC
preamble
dest.
address
source
address
preamble
data (payload)
CRC
type

## Slide 107: 利用以太网交换机可以很方便地 实现虚拟局域网
虚拟局域网 VLAN 是由一些局域网网段构成的与物理位置无关的逻辑组。
  这些网段具有某些共同的需求。
  每一个 VLAN 的帧都有一个明确的标识符，指明发送这个帧的工作站是属于哪一个 VLAN。
虚拟局域网其实只是局域网给用户提供的一种服务，而并不是一种新型局域网。

## Slide 108
以太网
交换机
A4
B1
以太网
交换机
VLAN3
C3
B3
VLAN1
VLAN2
C1
A2
A1
A3
C2
B2
以太网
交换机
以太网
交换机
三个虚拟局域网:
VLAN1, VLAN2 和 VLAN3

## Slide 109
以太网
交换机
A4
B1
以太网
交换机
VLAN3
C3
B3
VLAN1
VLAN2
C1
A2
A1
A3
C2
B2
以太网
交换机
以太网
交换机
三个虚拟局域网 VLAN1, VLAN2
和 VLAN3 的构成
当 B1 向 VLAN2 工作组内成员发送数据时，
工作站 B2 和 B3 将会收到广播的信息。

## Slide 110
以太网
交换机
A4
B1
以太网
交换机
VLAN3
C3
B3
VLAN1
VLAN2
C1
A2
A1
A3
C2
B2
以太网
交换机
以太网
交换机
三个虚拟局域网 VLAN1, VLAN2
和 VLAN3 的构成
B1 发送数据时，工作站 A1, A2 和 C1
都不会收到 B1 发出的广播信息。

## Slide 111
以太网
交换机
A4
B1
以太网
交换机
VLAN3
C3
B3
VLAN1
VLAN2
C1
A2
A1
A3
C2
B2
以太网
交换机
以太网
交换机
三个虚拟局域网 VLAN1, VLAN2
和 VLAN3 的构成
虚拟局域网限制了接收广播信息的工作站数，使得网络
不会因传播过多的广播信息(即“广播风暴”)而引起性能恶化。

## Slide 112: 高速以太网 100BASE-T 以太网
速率达到或超过 100 Mb/s 的以太网称为高速以太网。
在双绞线上传送 100 Mb/s 基带信号的星型拓扑以太网，仍使用 IEEE 802.3 的CSMA/CD 协议。100BASE-T 以太网又称为快速以太网(Fast Ethernet)。

## Slide 113: 100BASE-T 以太网的特点
可在全双工方式下工作而无冲突发生。因此，不使用 CSMA/CD 协议。
MAC 帧格式仍然是 802.3 标准规定的。
帧间时间间隔从原来的 9.6 s 改为现在的 0.96 s。

## Slide 114: 三种不同的物理层标准
100BASE-TX
  使用 2 对 UTP 5 类线或屏蔽双绞线 STP。
100BASE-FX
  使用 2 对光纤。
100BASE-T4
  使用 4 对 UTP 3 类线或 5 类线。

## Slide 115: 吉比特以太网
允许在 1 Gb/s 下全双工和半双工两种方式工作。
使用 802.3 协议规定的帧格式。
在半双工方式下使用 CSMA/CD 协议（全双工方式不需要使用 CSMA/CD 协议）。
与 10BASE-T 和 100BASE-T 技术向后兼容。

## Slide 116: 吉比特以太网的物理层
1000BASE-X 基于光纤通道的物理层：
  1000BASE-SX SX表示短波长
  1000BASE-LX LX表示长波长
  1000BASE-CX CX表示铜线
1000BASE-T
  使用 4对 5 类线 UTP

## Slide 117: 全双工方式
当吉比特以太网工作在全双工方式时（即通信双方可同时进行发送和接收数据），不使用载波延伸和分组突发。

## Slide 118: 吉比特以太网的配置举例
1 Gb/s 链路
吉比特
交换
集线器
百兆比特或吉比特集线器
100 Mb/s 链路
中央服务器

## Slide 119: 10 吉比特以太网
10 吉比特以太网与 10 Mb/s，100 Mb/s 和 1 Gb/s 以太网的帧格式完全相同。
10 吉比特以太网还保留了 802.3 标准规定的以太网最小和最大帧长，便于升级。
10 吉比特以太网不再使用铜线而只使用光纤作为传输媒体。
10 吉比特以太网只工作在全双工方式，因此没有争用问题，也不使用 CSMA/CD 协议。

## Slide 120: 吉比特以太网的物理层
局域网物理层 LAN PHY。局域网物理层的数据率是 10.000 Gb/s。
可选的广域网物理层 WAN PHY。广域网物理层具有另一种数据率，这是为了和所谓的“Gb/s”的 SONET/SDH（即OC-192/STM-64）相连接。
  为了使 10 吉比特以太网的帧能够插入到 OC-192/STM-64 帧的有效载荷中，就要使用可选的广域网物理层，其数据率为 9.95328 Gb/s。

## Slide 121: 端到端的以太网传输
10 吉比特以太网的出现，以太网的工作范围已经从局域网（校园网、企业网）扩大到城域网和广域网，从而实现了端到端的以太网传输。
这种工作方式的好处是：
  成熟的技术
  互操作性很好
  在广域网中使用以太网时价格便宜。
  统一的帧格式简化了操作和管理。

## Slide 122: 以太网从 10 Mb/s 到 10 Gb/s 的演进
以太网从 10 Mb/s 到 10 Gb/s 的演进证明了以太网是：
可扩展的（从 10 Mb/s 到 10 Gb/s）。
灵活的（多种传输媒体、全/半双工、共享/交换）。
易于安装。
稳健性好。

## Slide 123
2.7 PPP

## Slide 124: Point to Point Data Link Control
one sender, one receiver, one link: easier than broadcast link:
  no Media Access Control
  no need for explicit MAC addressing
  e.g., dialup link, ISDN line
popular point-to-point DLC protocols:
  PPP (point-to-point protocol)
  HDLC: High level data link control

## Slide 125
IP 数据报
1010… …0110
帧
取出
数据
链路层
网络层
链路
结点 A
结点 B
物理层
数据
链路层
结点 A
结点 B
帧
(a)
(b)
发送
帧
接收
链路
IP 数据报
1010… …0110
帧
装入
数据链路层传送的是帧

## Slide 126: 数据链路层像个数字管道
常常在两个对等的数据链路层之间画出一个数字管道，而在这条数字管道上传输的数据单位是帧。
早期的数据通信协议曾叫作通信规程(procedure)。因此在数据链路层，规程和协议是同义语。
结点
结点
帧
帧

## Slide 127: 数据链路层：三个基本问题
(1) 封装成帧
(2) 透明传输
(3) 差错控制

## Slide 128: 1. 封装成帧
封装成帧(framing)就是在一段数据的前后分别添加首部和尾部，然后就构成了一个帧。确定帧的界限。
首部和尾部的一个重要作用就是进行帧定界。
帧结束
帧首部
IP 数据报
帧的数据部分
帧尾部
 MTU
数据链路层的帧长
开始
发送
帧开始

## Slide 129: 用控制字符进行帧定界的方法举例
SOH
装在帧中的数据部分
帧
帧开始符
帧结束符
发送在前
EOT

## Slide 130: 2. 透明传输
SOH
EOT
出现了“EOT”
被接收端当作无效帧而丢弃
被接收端
误认为是一个帧
数据部分
EOT
完整的帧
发送
在前

## Slide 131: 解决透明传输问题
发送端的数据链路层在数据中出现控制字符“SOH” ”(其十六进制编码是 01)或“EOT” (其十六进制编码是 04)的前面插入一个转义字符“ESC”(其十六进制编码是 1B)。
字节填充(byte stuffing)或字符填充(character stuffing)——接收端的数据链路层在将数据送往网络层之前删除插入的转义字符。
如果转义字符也出现数据当中，那么应在转义字符前面插入一个转义字符。当接收端收到连续的两个转义字符时，就删除其中前面的一个。

## Slide 132: 用字节填充法解决透明传输的问题
SOH
SOH
EOT
SOH
ESC
ESC
EOT
ESC
SOH
ESC
ESC
ESC
SOH
原始数据
EOT
EOT
经过字节填充后发送的数据
字节填充
字节填充
字节填充
字节填充
发送
在前
帧开始符
帧结束符
SOH

## Slide 133: 3. 差错检测
在传输过程中可能会产生比特差错：1 可能会变成 0 而 0 也可能变成 1。
在一段时间内，传输错误的比特占所传输比特总数的比率称为误码率 BER (Bit Error Rate)。
误码率与信噪比有很大的关系。
为了保证数据传输的可靠性，在计算机网络传输数据时，必须采用各种差错检测措施。

## Slide 134: 用户到 ISP 的链路使用 PPP 协议
用
户
至因特网
已向因特网管理机构
申请到一批 IP 地址
ISP
接入网
PPP 协议

## Slide 135: PPP 协议的组成
1992 年制订了 PPP 协议。经过 1993 年和 1994 年的修订，现在的 PPP 协议已成为因特网的正式标准[RFC 1661]。
PPP 协议有三个组成部分
  一个将 IP 数据报封装到串行链路的方法。
  链路控制协议 LCP (Link Control Protocol)。
  网络控制协议 NCP (Network Control Protocol)。

## Slide 136: PPP Design Requirements [RFC 1557]
packet framing: encapsulation of network-layer datagram in data link frame
  carry network layer data of any network layer protocol (not just IP) at same time
  ability to demultiplex upwards
bit transparency: must carry any bit pattern in the data field
error detection (no correction)
connection liveness: detect, signal link failure to network layer
network layer address negotiation: endpoint can learn/configure each other’s network address

## Slide 137: PPP non-requirements
no error correction/recovery
no flow control
out of order delivery OK
no need to support multipoint links (e.g., polling)
Error recovery, flow control, data re-ordering
all relegated to higher layers!

## Slide 138
标志域 | 地址域 | 控制域 | 协议域 | 信息域 | 校验和 | 标志域
01111110 | 11111111 | 11111100 | 协议 | 信息 | 校验和 | 01111110
标识帧开始
1个字节7E
该字段目
前无作用
传输的
数据
标识帧结束
1个字节7E
标识目的地址,不起作用
上层协议，1/2字节：
LCP-C021， IPCP-
8021，IP-0021,
DECnet-027 ,
AppleTalk-0029
差错检查：
16/32-CRC，

## Slide 139: PPP Data Frame
Flag: delimiter (framing)
Address: does nothing (only one option)
Control: does nothing; in the future possible multiple control fields
Protocol: upper layer protocol to which frame delivered (eg, PPP-LCP, IP, IPCP, etc)

## Slide 140: PPP Data Frame
info: upper layer data being carried
check: cyclic redundancy check for error detection

## Slide 141: Byte Stuffing
“data transparency” requirement: data field must be allowed to include flag pattern <01111110>
  Q: is received <01111110> data or flag?
Sender: adds (“stuffs”) extra < 01111110> byte after each < 01111110> data byte
Receiver:
  two 01111110 bytes in a row: discard first byte, continue data reception
  single 01111110: flag byte

## Slide 142: 字节填充举例
标志域 | 地址域 | 控制域 | 协议域 | 信息域 | 校验和 | 标志域
01111110 | 11111111 | 11111100 | 协议 | 信息 | 校验和 | 01111110
01111110 | 11111111 | 11111100 | 00100001 | 01111110 | 校验和 | 01111110
01111110 | 11111111 | 11111100 | 00100001 | 01111101 01111110 | 校验和 | 01111110
字节填充
发送前
发送数据
01111110 | 11111111 | 11111100 | 00100001 | 01111101 01111110 | 校验和 | 01111110
01111110 | 11111111 | 11111100 | 00100001 | 01111110 | 校验和 | 01111110
接收数据处理

## Slide 143: Byte Stuffing
flag byte
pattern
in data
to send
flag byte pattern plus
stuffed byte in transmitted data

## Slide 144: PPP Data Control Protocol
Before exchanging network-layer data, data link peers must
configure PPP link (max. frame length, authentication)
learn/configure network
layer information
  for IP: carry IP Control Protocol (IPCP) msgs (protocol field: 8021) to configure/learn IP address

## Slide 145: PPP 协议的工作状态
当用户拨号接入 ISP 时，路由器的调制解调器对拨号做出确认，并建立一条物理连接。
PC 机向路由器发送一系列的 LCP 分组（封装成多个 PPP 帧）。
这些分组及其响应选择一些 PPP 参数，和进行网络层配置，NCP 给新接入的 PC机分配一个临时的 IP 地址，使 PC 机成为因特网上的一个主机。
通信完毕时，NCP 释放网络层连接，收回原来分配出去的 IP 地址。接着，LCP 释放数据链路层连接。最后释放的是物理层的连接。

## Slide 146
设备之间无链路
链路静止
链路建立
鉴别
网络层协议
链路打开
链路终止
物理链路
LCP 链路
已鉴别的 LCP 链路
已鉴别的 LCP 链路
和 NCP 链路
物理层连接建立
LCP 配置协商
鉴别成功或无需鉴别
NCP 配置协商
链路故障或
关闭请求
LCP 链路
终止
鉴别失败
LCP 配置
协商失败
Notes: 链路管理