## Slide 1
Computer Networking: A Top Down Approach
7th Edition, Global Edition Jim Kurose, Keith Ross Pearson April 2016
ISBN: 978-0133594140
Computer Networks
Lectured by：LIU Yixian
Software College
Northeastern University
Email：liuyx@swc.neu.edu.cn

## Slide 2: 课程介绍：
一、课程内容
1、网络概况
2、以太网
3、TCP/IP协议、网络层和传输层
4、网络互联
5、网络新技术

## Slide 3
三、学习方法
1、广泛阅读资料
2、大量参考案例
3、可自学
四、参考资料
1． James F. Kurose, Keith W. Ross, 计算机网络：自顶向下方法（原书第7版），机械工业出版社，2017.
2. Andrew S. Tanenbaum, David J. Wetherall, Computer Networks (5th edition), 机械工业出版社。
3．谢希仁著：《计算机网络（第7版）》，电子工业出版社，2018。
4. 唐纳德.斯蒂文,TCP/IP协议祥解,电子工业出版社

## Slide 4
五、成绩评定
1、出勤率（10%）
2、平时测验与作业（40%）
3、期末考试（50%）

## Slide 5: Chapter 1: Introduction
Our goal:
get “feel” and terminology
more depth, detail later in course
approach:
  use Internet as example
Overview:
what’s the Internet
what’s a protocol?
network edge
network core
access net, physical media
Internet/ISP structure
performance: loss, delay
protocol layers, service models
network modeling

## Slide 6: Terms in chapter 1
LAN 局域网
WAN 广域网
Router 路由器
Switch 交换机
Protocol 协议
Packet 数据包/报文/分组
ISP 因特网服务提供商
TCP 传输控制协议
UDP 用户数据报协议
Intranet内网
Bandwidth 带宽
infrastructure 基础设施
Ethernet 以太网
Multiplexing 多路复用
Encapsulation 封装
Stack 栈
FDM 频分复用
TDM 时分复用
congestion 拥挤拥塞
Extranet 外网
Notes: TCP: Transmission Control Protocol
UDP: User Datagram Protocol
ISP: Internet Service Provider
LAN: Local Area Network
WAN: Wide Area Network
FDM: Frequency Division Multiplexing
TDM: Time Division Multiplexing

## Slide 7: Chapter 1: Roadmap
  1.1 What is the Internet?
  1.2 Internet History
  1.3 Network edge
    End systems, access network, links
  1.4 Network core
    Packet switching, circuit switching, network structure
  1.5 Network access and physical media
  1.6 Internet structure and ISPs
  1.7 Delay & loss in packet-switched networks
  1.8 Protocol layers, service models
  1.9 Network Security

## Slide 8: Category of Computer Networks
Computer Networks
  A computer network is composed of multiple computers connected together using a telecommunication system for the purpose of sharing data, resources and communication.
  1.1 What is the Internet?
Definition from Wikipedia: A computer network or data network is a digital telecommunications network which allows nodes to share resources. In computer networks, networked computing devices exchange data with each other using a data link.
Notes: 连通性和共享性，是基本功能
计算机网络
  一般地说，将分散的多台计算机、终端和外部设备用通信线路互联起来，彼此间实现互相通信，并且计算机的硬件、软件和数据资源大家都可以共同使用，实现资源共享的整个系统就叫做计算机网络。

## Slide 9
Computer network connects two or more autonomous computers.
The computers can be geographically located anywhere.
Two computers are said to be interconnected if they are able to exchange information.
Network comes in many sizes, shapes and forms.
Computer Networks
Notes: Autonomous computer is composed of software and hardware, can independently implement various functions.
Interconnected with communication models and interfaces.
Computer networks connected together to compose larger networks.
Internet : the most well-known example of a network of networks.

## Slide 10
Composition of Computer Network
Hardware
  End Systems: Host, PC, Mainframe(大型机), Client, Workstation, Server
  Intermediate Systems: Communications: Switch, Router
  Interface: Network interface card(NIC), Modem
  Medium: Twisted pair, Coaxial cable, Fiber, Wireless
Software
  Protocol: CSMA/CD, TCP/IP, UDP, PPP, ATM
  Applications: HTTP, SMTP, FTP, Telnet

## Slide 11
Applications of Networks
Resource Sharing
  Hardware (computing resources, disks, printers)
  Software (application software)
Information Sharing
  Easy accessibility from anywhere (files, databases)
  Search Capability (WWW)
Communication
  Email
  Message broadcast
Ubiquitous computing(普适计算)
Mobile Users
  802.11 hotspot, 3G and 4G, wearable computer

## Slide 12
Applications
E-mail
Searchable Data (Web Sites)
E-Commerce
News Groups
Internet Telephony (VoIP)
Video Conferencing
Chat Groups
Instant Messengers
Internet Radio
Game

## Slide 13: “Cool” internet appliances
IP picture frame
http://www.ceiva.com/
Web-enabled toaster +
weather forecaster
Internet phones
Internet
refrigerator
Slingbox: watch,
control cable TV remotely
sensorized,
bed
mattress
Air cleaner
Tweet-a-watt:
monitor energy use

## Slide 14
Classified by Topology
The network topology defines the way in which computers, printers, and other devices are connected. A network topology describes the layout of the wire and devices as well as the paths used by data transmissions.
Category of Computer Networks

## Slide 15: Bus Topology
Commonly referred to as a linear bus, all the devices on a bus topology are connected by one single cable.

## Slide 16: Star & Tree Topology
The star topology is the most commonly used architecture in Ethernet LANs.
When installed, the star topology resembles spokes in a bicycle wheel.
Larger networks use the extended star topology also called tree topology. When used with network devices that filter frames or packets, like bridges, switches, and routers, this topology significantly reduces the traffic on the wires by sending packets only to the wires of the destination host.

## Slide 17: Ring Topology
A frame travels around the ring, stopping at each node. If a node wants to transmit data, it adds the data as well as the destination address to the frame.
The frame then continues around the ring until it finds the destination node, which takes the data out of the frame.
  Single ring – All the devices on the network share a single cable
  Dual ring – The dual ring topology allows data to be sent in both directions.

## Slide 18: Category of Computer Networks
Classified by scale
  LAN(MAN)
    A local area network (LAN) is a group of computers and associated devices that share a common communications line or wireless link within a small geographic area.
  WAN
    A wide area network (WAN) is a geographically dispersed telecommunications network. The term distinguishes a broader telecommunication structure from a local area network (LAN).
  Internet
    a worldwide system of computer networks - a network of networks in which users at any one computer can, if they have permission, get information from any other computer, even use the remote computers.

## Slide 19: Category of Computer Networks
Classified by boundary
  Intranet （Private Networks）
    An intranet is a private network that is contained within an enterprise. It may consist of many interlinked local area networks and also use leased lines in the wide area network.
  Extranet （Public Networks）
    An extranet is a private network that uses Internet technology and the public telecommunication system to securely share part of a business's information or operations with suppliers, vendors, partners, customers, or other businesses. An extranet can be viewed as part of a company's intranet that is extended to users outside the company. It has also been described as a "state of mind" in which the Internet is perceived as a way to do business with other companies as well as to sell products to customers.

## Slide 20: What’s the Internet?
billions of connected computing devices: hosts = end systems
running network apps
communication links
  fiber, copper, radio, satellite
  transmission rate = bandwidth
routers: forward packets (chunks of data)
“nuts and bolts” view
mobile network
global ISP
regional ISP
home
network
institutional
network
Notes: nuts and bolts：基本要点
通信链路：同轴电缆、铜线、光纤、无线电频谱，不同速率传输数据。传输速率bps。
分组交换机：路由器和链路层交换机。向目的地转发分组。分组经历的通信链路和分组交换机成为路径。承载运输车辆的运输网络，一堆货物，首先分成几份，装车。桥和路口可以看做是分组交换机，路牌可以看做转发表，目的地卸下货物，重新堆放在一起。

## Slide 21: What’s the Internet: “nuts and bolts” view
protocols control sending, receiving of msgs
  e.g., TCP, IP, HTTP, FTP, PPP
Internet: “network of networks”
  loosely hierarchical
  public Internet versus private intranet
Internet standards
  RFC: Request for comments
  IETF: Internet Engineering Task Force
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 22: A closer look at network structure:
network edge: applications and hosts
access networks, physical media: wired, wireless communication links
network core:
  interconnected routers
  network of networks
mobile network
global ISP
regional ISP
home
network
institutional
network
Notes: 从具体构成描述。因特网是世界范围的计算机网络。

## Slide 23: What’s the Internet: a service view
communication infrastructure enables distributed applications:
  Web, email, games, e-commerce, file sharing
communication services provided to apps:
  Connectionless unreliable
  connection-oriented reliable
Question：other sevices？
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 24: What’s a protocol?
human protocols:
“what’s the time?”
“I have a question”
introductions
… specific msgs sent
… specific actions taken when msgs received, or other events
network protocols:
machines rather than humans
all communication activity in Internet governed by protocols
protocols define format, order of msgs sent and received among network entities, and actions taken on msg transmission, receipt
Notes: 人类活动。发送的特定报文，也有我们根据接收的应答报文或其他时间采取的动作。一人礼貌，一人不礼貌，不明白问题概念，或不知道。协议不能互动。要求两个实体运行相同的协议。 提问与问题协议的核心。
定义了两个或多个网络实体之间交换的报文格式和顺序，以及报文发送或接收一条报文或其他事件采取的动作。

## Slide 25: What’s a protocol?
a human protocol and a computer network protocol:
Q: Other human protocols?
Hi
Hi
Got the
time?
2:00
TCP connection
request
TCP connection
response
Get http://www.awl.com/kurose-ross
<file>
time
Notes: 淘宝
向Web服务器发出请求，URL.
报文交换以及发送和接收报文采取的动作是定义协议的关键

## Slide 26: 1.2 Internet History
1961: Kleinrock - queueing theory shows effectiveness of packet-switching
1964: Baran - packet-switching in military nets
1967: ARPAnet conceived by Advanced Research Projects Agency
1969: first ARPAnet node operational
1972:
  ARPAnet public demonstration
  NCP (Network Control Protocol) first host-host protocol
  first e-mail program
  ARPAnet has 15 nodes
1961-1972: Early packet-switching principles

## Slide 27
1970: ALOHAnet satellite network in Hawaii
1974: Cerf and Kahn - architecture for interconnecting networks
1976: Ethernet at Xerox PARC
ate70’s: proprietary architectures: DECnet, SNA, XNA
late 70’s: switching fixed length packets (ATM precursor)
1979: ARPAnet has 200 nodes
Cerf and Kahn’s internetworking principles:
  minimalism, autonomy - no internal changes required to interconnect networks
  best effort service model
  stateless routers
  decentralized control
define today’s Internet architecture
1972-1980: Internetworking, new and proprietary nets

## Slide 28
1983: deployment of TCP/IP
1982: smtp e-mail protocol defined
1983: DNS defined for name-to-IP-address translation
1985: ftp protocol defined
1988: TCP congestion control
new national networks: Csnet, BITnet, NSFnet, Minitel
100,000 hosts connected to confederation of networks
1980-1990: new protocols, a proliferation of networks

## Slide 29
Early 1990’s: ARPAnet decommissioned
1991: NSF lifts restrictions on commercial use of NSFnet (decommissioned, 1995)
early 1990s: Web
  hypertext [Bush 1945, Nelson 1960’s]
  HTML, HTTP: Berners-Lee
  1994: Mosaic, later Netscape
  late 1990’s: commercialization of the Web
Late 1990’s – 2000’s:
more killer apps: instant messaging, P2P file sharing
network security to forefront
est. 50 million host, 100 million+ users
backbone links running at Gbps
1990, 2000’s: commercialization, the Web, new apps

## Slide 30
2005-present
About 5 billion devices attached to Internet (2016)
  smartphones and tablets
aggressive deployment of broadband access
increasing ubiquity of high-speed wireless access
emergence of online social networks:
  Facebook: ~ one billion users
service providers (Google, Microsoft) create their own networks
  bypass Internet, providing “instantaneous” access to search, video content, email, etc.
e-commerce, universities, enterprises running their services in “cloud” (e.g., Amazon EC2)

## Slide 31: Timothy B. Lee , 40 maps that explain the internet, https://www.vox.com/a/internet-maps, 2014.

## Slide 32: www.internetworldstats.com

## Slide 33
IETF (Internet Engineering Task Force), http://www.ietf.org
  Internet Society, http://www.isoc.org
  IAB(Internet Architecture Board), http://www.isi.edu/iab
W3C (The world Wide Web Consortium), www.w3.org/consortium
ACM (Association for Computing Machine), http://www.acm.org/
  IEEE, http://www.ieee.org
  SIGCOMM, http://www.acm.org/sigcomm
  IEEE Communications Society, http://www.comsoc.org
  IEEE Computer Society, http://www.computer.org
Data Communications tutorials, http://www.data.com
Media History Project, http://www.mediahistory.com

## Slide 34: A closer look at network structure:
network edge: applications and hosts
network core:
  routers
  network of networks
access networks, physical media: communication links
  1.3 Network edge

## Slide 35: The network edge:
end systems (hosts):
  run application programs
  e.g. Web, email
  at “edge of network”
client/server model
  client host requests, receives service from always-on server
  e.g. Web browser/server; email client/server
peer-peer model:
  minimal (or no) use of dedicated servers
  e.g. Gnutella, KaZaA, Skype

## Slide 36: Network edge: connection-oriented service
connection-oriented service,
What is Connection？
  the devices at the end points use a protocol to establish an end-to-end logical or physical connection before any data may be sent. Connection Oriented protocol provides its services during the following three steps or processes: Handshaking, Data Transfer, Connection Termination.
(
(
(
(
switch
switch
switch
switch
subscriber line
subscriber line
trunk line
trunk line
B
D
C
A

## Slide 37: Network edge: connection-oriented service
Goal: data transfer between end systems
handshaking: setup (prepare for) data transfer ahead of time
  Hello, hello back human protocol
  set up “state” in two communicating hosts
TCP - Transmission Control Protocol
  Internet’s connection-oriented service
TCP service [RFC 793]
reliable, in-order byte-stream data transfer
  loss: acknowledgements and retransmissions
flow control（流控制）
  sender won’t overwhelm receiver
congestion control: （拥塞控制）
  senders “slow down sending rate” when network congested
如果数据丢失了，
怎么办？
TCP is a key protocol in the Internet.
We will introduce it in Chapter 3。

## Slide 38: Network edge: connectionless service
connectionless service，
  A service in which there is no need for connection setup between devices for transferring data.
  A device sends data to another device whenever it has data to send.
  This service does not provide reliable transfer service.

## Slide 39: Network edge: connectionless service
Goal: data transfer between end systems
  same as before!
UDP - User Datagram Protocol [RFC 768]:
  connectionless
  unreliable data transfer
  no flow control
  no congestion control
App’s using TCP:
HTTP (Web), FTP (file transfer), Telnet (remote login), SMTP (email)
App’s using UDP:
streaming media, teleconferencing, DNS, Internet telephony
QQ

## Slide 40: 1.4 The Network Core
Mesh of interconnected routers
the fundamental question: how is data transferred through net?
  circuit switching:
    dedicated circuit per call: telephone net
  packet-switching:
    data sent thru net in discrete “chunks”

## Slide 41: Network Core: Circuit Switching
End-end resources reserved for “call”
link bandwidth, switch capacity
dedicated resources: no sharing
circuit-like (guaranteed) performance
call setup required

## Slide 42
end-end resources allocated to, reserved for “call” between source & dest:
in diagram, each link has four circuits.
  call gets 2nd circuit in top link and 1st circuit in right link.
dedicated resources: no sharing
  circuit-like (guaranteed) performance
circuit segment idle if not used by call (no sharing)
commonly used in traditional telephone networks

## Slide 43: Network Core: Circuit Switching
connection-oriented service
The circuit guarantees the full bandwidth of the channel and remains connected for the duration of the communication session
Transmission efficiency of Circuit switching for computer data? WHY?
telecommunication network
Provides reliable delivery service

## Slide 44: Network Core: Circuit Switching
network resources (e.g., bandwidth) divided into “pieces”
pieces allocated to calls
resource piece idle if not used by owning call (no sharing)
Multiplexing:多工，复用
dividing link bandwidth into “pieces”
How to divide？
  frequency division
    FDM
  time division
    TDM
  code division
    CDMA
Notes: 在电路交换网络中，资源分成片，每一片分给不同的调用。这样导致如果当前资源空闲。

## Slide 45: Example of FDM
FM broadcast：
  Band：88－108MHz
  Bandwidth？
  How many radio station?

## Slide 46: Circuit Switching: FDM and TDM
FDM
frequency
time
TDM
frequency
time
4 users
Example:

## Slide 47: TDM
f
t
B
C
D
B
C
D
B
C
D
B
C
D
A
A
A
A
Fixed position
TDM
TDM
TDM
TDM
…
TDM

## Slide 48: TDM
f
t
C
D
C
D
C
D
A
A
A
A
B
B
B
B
C
D
Fixed position
TDM
TDM
TDM
TDM
…
TDM

## Slide 49: TDM
f
t
B
D
B
D
B
D
A
A
A
A
B
C
C
C
C
D
Fixed position
TDM
TDM
TDM
TDM
…
TDM

## Slide 50: TDM
f
t
B
C
B
C
B
C
A
A
A
A
B
C
D
D
D
D
Fixed position
TDM
TDM
TDM
TDM
…
TDM

## Slide 51: TDM of E1
2.048 Mb/s
传输线路
CH0
CH16
CH17
CH15
CH15
CH16
CH17
CH31
CH31
CH0
CH1
CH1
…
…
…
…
时分复用帧
T
CH0
CH1
CH2
…
CH15
CH16
CH17
CH30
CH31
CH0
…
8 bit
t
时分复用帧
时分复用帧
T = 125 ms
15 个话路
15 个话路

## Slide 52: waste resources?
A
B
C
D
a
a
b
b
c
d
b
c
a
t
t
t
t
t
TDM Frame
#1
④
③
②
①
a
c
b
c
d
TDM
#2
#3
#4
user

## Slide 53: Numerical example
How long does it take to send a file of 640K bits from host A to host B over a circuit-switched network?
  All links are 1.536 Mbps
  Each link uses TDM with 24 slots/sec
  500 msec to establish end-to-end circuit
Let’s work it out!
Transmission rate：1.536Mbps÷24=64Kbps
Transmission time：640K÷64Kbps=10s
Creation time：0.5s
Total time＝10.5s
Notes: 传输速度
传输时间
创建时间
发送文件时间

## Slide 54: Another numerical example
How long does it take to send a file of 640,000 bits from host A to host B over a circuit-switched network?
  All links are 1.536 Mbps
  Each link uses FDM with 24 channels/frequencies
  500 msec to establish end-to-end circuit
Let’s work it out!
Transmission rate：1.536Mbps÷24＝64Kbps
Transmission time：640K÷64Kbps=10s
Creation time：0.5s
Total=10.5s

## Slide 55: Network Core: Packet Switching
each end-end data stream divided into packets
user A, B packets share network resources
each packet uses full link bandwidth
resources used as needed
resource contention:
aggregate resource demand can exceed amount available
congestion: packets queue, wait for link use
store and forward: packets move one hop at a time
  Node receives complete packet before forwarding
Bandwidth division into “pieces”
Dedicated allocation
Resource reservation

## Slide 56: Network Core: Packet Switching

## Slide 57: Packet Switching: Statistical Multiplexing
Sequence of A & B packets does not have fixed pattern, shared on demand  statistical multiplexing.
TDM: each host gets same slot in revolving TDM frame.
A
B
C
10 Mb/s
Ethernet
1.5 Mb/s
D
E
statistical multiplexing
queue of packets
waiting for output
link
Notes: 统计复用

## Slide 58: STDM: Statistical time division multiplexing
User
A
B
C
D
a
b
c
d
t
t
t
t
t
3 个 STDM
#1
④
③
②
①
a
c
b
a
b
b
c
a
c
d
#2
#3
STDM
Notes: 为了提高TDM系统的利用率,可以使用按需分配的技术,即根据用户需求动态分配时隙,以避免每帧中出现空闲的时隙.此时复用器传输的数据只来自正在工作的设备,这种动态分配时隙的工作方式称为统计时分复用(Statistical Time Division Multiplexing,STDM).

## Slide 59: Packet switching versus circuit switching
1 Mb/s link
each user:
  100 kb/s when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active less than .0004
Packet switching allows more users to use network!
Q: how did we get value 0.0004?
N
users
1 Mbps link
…..

## Slide 60: Packet switching versus circuit switching
Great for bursty data
  resource sharing
  simpler, no call setup
Excessive congestion: packet delay and loss
  protocols needed for reliable data transfer, congestion control
Q: How to provide circuit-like behavior?
  bandwidth guarantees needed for audio/video apps
  still an unsolved problem (chapter 7)
Is packet switching a “slam dunk winner?”
Q: human analogies of reserved resources (circuit switching) versus on-demand allocation (packet-switching)?
Notes: slam dunk winner 大满贯
若要连续传送大量数据，且传送时间远大于建立连接时间，则电路交换的传输速率较快。分组交换不需要预先分配传输带宽，在传送突发数据时可提高整个网络的信道利用率。
分组交换存在问题：分组在各路由器存储转发时需要排队，造成一定的时延。无法确保通信时端到端的带宽。
各分组携带控制信息造成一定的开销。需要专门的管理和控制机制。

## Slide 61: Packet-switching: store-and-forward
Takes L/R seconds to transmit (push out) packet of L bits on to link or R bps
Entire packet must arrive at router before it can be transmitted on next link: store and forward
delay = 3L/R (assuming zero propagation delay)
Example:
L = 7.5 Mbits
R = 1.5 Mbps
delay = 15 sec
R
R
R
L
more on delay shortly …

## Slide 62: Packet-switching: store-and-forward
Takes L/R seconds to transmit (push out) packet of L bits on to link or R bps
Entire packet must arrive at router before it can be transmitted on next link: store and forward
delay = 3L/R
Example:
L = 7.5 Mbits
R = 1.5 Mbps
delay = 15 sec
R
R
R
L
more on delay shortly …
L=7.5M
l(packet)=1.5K
Delay=?

## Slide 63: Packet-switched networks: forwarding
Goal: move packets through routers from source to destination
  we’ll study several path selection (i.e. routing) algorithms (chapter 4)
datagram network:
  destination address in packet determines next hop
  routes may change during session
  analogy: driving, asking directions
virtual circuit network:
  each packet carries tag (virtual circuit ID), tag determines next hop
  fixed path determined at call setup time, remains fixed thru call
  routers maintain per-call state

## Slide 64: Network Taxonomy
Datagram network is not either connection-oriented
or connectionless.
Internet provides both connection-oriented (TCP) and
connectionless services (UDP) to apps.
What’s the difference
between TDM and FDM?
Telecommunication
networks
Circuit-switched
networks
FDM
TDM
Packet-switched
networks
Networks
with VCs
Datagram
Networks
CDM
Notes: 分类

## Slide 65: Access networks and physical media
Q: How to connect end systems to edge router?
residential access nets
institutional access networks (school, company)
mobile access networks
Keep in mind:
bandwidth (bits per second) of access network?
shared or dedicated?
where are you going to access the networks?
which ISP?
  1.4 Network access and physical media

## Slide 66: Residential access: point to point access
Dialup via modem
  up to 56Kbps direct access to router (often less)
  Can’t surf and phone at same time: can’t be “always on”

## Slide 67: Residential access: Asymmetric Digital Subscriber Line(ADSL)
  use existing telephone line to central office DSLAM
    data over DSL phone line goes to Internet
    voice over DSL phone line goes to telephone net
  < 2.5 Mbps upstream transmission rate (typically < 1 Mbps)
  < 24 Mbps downstream transmission rate (typically < 10 Mbps)
ISP
central office
telephone
network
DSLAM
voice, data transmitted
at different frequencies over
dedicated line to central office
DSL
modem
splitter
DSL access
multiplexer

## Slide 68: Residential access: cable modems
HFC: hybrid fiber coax（混和光纤同轴电缆）
  asymmetric: up to 30Mbps downstream, 2 Mbps upstream
network of cable and fiber attaches homes to ISP router
  homes share access to router
deployment: available via cable TV companies

## Slide 69: Residential access: cable modems

## Slide 70: Residential access: cable modems
  fiber optics connect the cable head end to neighborhood-level junctions.
  Traditional coaxial cable is then used to reach individual houses and apartments.

## Slide 71: Cable Network Architecture: Overview
home
cable headend
cable distribution
network (simplified)
Typically 500 to 5,000 homes

## Slide 72: Cable Network Architecture: Overview
home
cable headend
cable distribution
network
server(s)

## Slide 73: Cable Network Architecture: Overview
home
cable headend
cable distribution
network (simplified)

## Slide 74: Cable Network Architecture: Overview
cable
modem
splitter
…
cable headend
Channels
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
D
A
T
A
D
A
T
A
C
O
N
T
R
O
L
1
2
3
4
5
6
7
8
9
frequency division multiplexing: different channels transmitted
in different frequency bands

## Slide 75
ISP
data, TV transmitted at different
frequencies over shared cable
distribution network
cable
modem
splitter
…
cable headend
CMTS
cable modem
termination system
HFC: hybrid fiber coax
  asymmetric: up to 30Mbps downstream transmission rate, 2 Mbps upstream transmission rate
network of cable, fiber attaches homes to ISP router
  homes share access network to cable headend
  unlike DSL, which has dedicated access to central office
Access network: cable network

## Slide 76
Access network: home network
to/from headend or central office
cable or DSL modem
router, firewall, NAT
wired Ethernet (1 Gbps)
wireless access
point (54 Mbps)
wireless
devices
often combined
in single box

## Slide 77: FTTx technology
FTTH(Fiber To the Home):光纤一直铺设到用户家庭可能是居民接入网最后的解决方法。
FTTB(Fiber to the Building):光纤进入大楼后就转换为电信号，然后用电缆或双绞线分配到各用户。
FTTC( Fiber to the Curb):从路边到各用户可使用星形结构双绞线作为传输媒体。

## Slide 78: Enterprise Network Access: local area networks(Ethernet)
Ethernet
switch
institutional mail,
web servers
institutional router
institutional link to
ISP (Internet)
  typically used in companies, universities, etc.
  10 Mbps, 100Mbps, 1Gbps, 10Gbps transmission rates
  today, end systems typically connect into Ethernet switch

## Slide 79: Wireless access networks
shared wireless access network connects end system to router
  via base station aka “access point”
wireless LANs:
  within building (100 ft.)
  802.11b/g/n (WiFi): 11, 54, 450 Mbps transmission rate
wide-area wireless access
  provided by telco (cellular) operator, 10’s km
  between 1 and 10 Mbps
  3G, 4G: LTE
to Internet
to Internet

## Slide 80: Physical Media
Bit: propagates between transmitter/rcvr pairs
physical link: what lies between transmitter & receiver
guided media:
  signals propagate in solid media: copper, fiber, coax
unguided media:
  signals propagate freely, e.g., radio

## Slide 81
铜线
聚氯乙烯
套层
屏蔽层
绝缘层
屏蔽双绞线 STP
铜线
聚氯乙烯 套层
绝缘层
无屏蔽双绞线 UTP
Twisted Pair (TP)
two insulated copper wires
  Category 3: traditional phone wires, 10 Mbps Ethernet
  Category 5: 100Mbps, 1 Gbps Ethernet
  Category 6: 10 Gbps Ethernet

## Slide 86
目前，在局域网中常用到的双绞线是非屏蔽双绞线（UTP），它又分：3类、4类、5类、超5类、6类和7类。
双绞线的这8根线的引脚定义如下：
线路线号
1
2
3
4
5
6
7
8
线路色标
白绿
绿
白橙
蓝
白蓝
橙
白褐
褐
引脚定义
Tx+
Tx-
Rx+
Rx-

## Slide 87
二者没有本质的区别，只是颜色上的区别 ，只要保证：
1,2 线对是一个绕对 3,6 线对是一个绕对
4,5 线对是一个绕对 7,8 线对是一个绕对
注意：不要在电缆一端用T568A，另一端用T568B
T568A/T568B的混用是跨接线的特殊接线方法

## Slide 88
常规双绞线接法两端都用T568a
交叉线双绞线接法一端T568a一端T568b

## Slide 89
直连线
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8

## Slide 90
交叉线
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8

## Slide 91: Physical Media: coax
Coaxial cable:
two concentric copper conductors
bidirectional
baseband:
  single channel on cable
  legacy Ethernet
broadband:
  multiple channels on cable
  HFC

## Slide 92: Physical Media: fiber
Fiber optic cable:
glass fiber carrying light pulses, each pulse a bit
high-speed operation:
  high-speed point-to-point transmission (e.g., 10’s-100’s Gps)
low error rate: repeaters spaced far apart ; immune to electromagnetic noise

## Slide 93: Physical media: radio
signal carried in electromagnetic spectrum
no physical “wire”
Bidirectionalpropagation environment effects:
  reflection
  Obstruction by objects
  Interference
Radio link types:
terrestrial microwave
  e.g. up to 45 Mbps channels
LAN (e.g., Wifi)
  2Mbps, 11Mbps, 54 Mbps
wide-area (e.g., cellular)
  e.g. 3G: hundreds of kbps
satellite
  Kbps to 45Mbps channel (or multiple smaller channels)
  270 msec end-end delay
  geosynchronous versus low altitude

## Slide 94: Assignments 1
1. Summarize different approaches of accessing networks, and properties of them. Write a report no less than 800 words, in either English or Chinese.
Hand in this report next time.

## Slide 95: Internet structure: network of networks
roughly hierarchical
at center: “tier-1” ISPs (e.g., MCI, Sprint, AT&T, Cable and Wireless), national/international coverage
  treat each other as equals
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-1 providers interconnect (peer) privately
NAP
Tier-1 providers also interconnect at public network access points (NAPs)
  1.6 Internet structure and ISPs

## Slide 96: Tier-1 ISP: e.g., Sprint
Sprint US backbone network
Seattle
Atlanta
Chicago
Roachdale
Stockton
San Jose
Anaheim
Fort Worth
Orlando
Kansas City
Cheyenne
New York
Pennsauken
Relay
Wash. DC
Tacoma
DS3 (45 Mbps)
OC3 (155 Mbps)
OC12 (622 Mbps)
OC48 (2.4 Gbps)
…
to/from customers
peering
to/from backbone
….
…
…
…
POP: point-of-presence

## Slide 97: Internet structure: network of networks
“Tier-2” ISPs: smaller (often regional) ISPs
  Connect to one or more tier-1 ISPs, possibly other tier-2 ISPs
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
NAP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP pays tier-1 ISP for connectivity to rest of Internet
tier-2 ISP is customer of
tier-1 provider
Tier-2 ISPs also peer privately with each other, interconnect at NAP

## Slide 98: Internet structure: network of networks
“Tier-3” ISPs and local ISPs
  last hop (“access”) network (closest to end systems)
校园网
校园网
校园网
校园网
校园网
校园网
国家主干网
地区网
地区网
地区网

## Slide 99: UMass Campus Network

## Slide 100: Internet structure: network of networks
a packet passes through many networks!
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
NAP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP

## Slide 101: Internet structure: network of networks
a packet passes through many networks!
大公司
地区 ISP
网络接入点
NAP
（对等点）
公司
校园网
主干服务
提供者
校园网
校园网
校园网
校园网
本地 ISP
地区 ISP
地区 ISP
地区 ISP
本地 ISP
本地 ISP
大公司
大公司
网络接入点
NAP
（对等点）

## Slide 102: Internet structure: network of networks
The Internet of 2012
  Content provider network, e.g. google

## Slide 103: A question
Assume two links with transmission rate of 10Mb and 100Mb, which is faster for transmitting 1 bit.
Why？
  1.7 Delay & loss in packet-switched networks
10MBps
100MBps

## Slide 104: Performance of Computer network
Data rate(数据率)：计算机网络上的主机在数字信道上的传送数据的速率。
  100M Ethernet
Bandwidth(带宽）
    Frequency
    Transmission rate
  Throughput(吞吐量)
    rate (bits/time unit) at which bits transferred between sender/receiver
    Restricted by rated speed(额定速率)

## Slide 105: Communication channel
Either to a physical transmission medium such as a wire, or to a logical connection over a multiplexed medium such as a radio channel.
  convey an information signal from one or several senders (or transmitters) to one or several receivers
  capacity for transmitting information-- bandwidth in Hz or its data rate in bits per second

## Slide 106: Communication channel
One-way communication:
    transmitted from one point to another or to many points simultaneously.
    no reception of information at the transmitting point and no transmission of information from a receiving point.
  Half-duplex
    communication in both directions, but only one direction at a time
  Full-duplex
    allows communication in both directions

## Slide 107: How do loss and delay occur?
packets queue in router buffers
packet arrival rate to link exceeds output link capacity
packets queue, wait for turn
A
B
packet being transmitted (delay)
packets queueing (delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 108: Four sources of packet delay
1. nodal processing:
  check bit errors
  determine output link
2. queueing
  time waiting at output link for transmission
  depends on congestion level of router
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission

## Slide 109: Delay in packet-switched networks
3. Transmission delay:
R=link bandwidth (bps)
L=packet length (bits)
time to send bits into link = L/R
4. Propagation delay:
d = length of physical link
s = propagation speed in medium (~2x108 m/sec)
propagation delay = d/s
Note: s and R are very different quantities!
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission

## Slide 110: Numerical example
两个主机A、B相距L＝10000Km，由一条直接的带宽R＝1Mbps（220）的链路相连接，假定跨越该链路的传播速度V＝2.5×108mps
  传播时延Tp是多少？
  在这段时间里，主机A向链路中发送了多少个bit？
  Bit与Bit之间的间距l有多长？
Tp＝L÷？＝
Numb＝Tp×？=
l＝L÷ Numb＝？
Tp＝L÷V＝0.04s
Numb＝Tp× R=41943
l＝L÷ Numb＝238m
Question：假设l＝10000Km，那么R＝？
L÷V×R是什么含义？
（时延带宽积）

## Slide 111: Caravan analogy
Cars “propagate” at 100 km/hr
Toll booth takes 12 sec to service a car (transmission time)
car~bit; caravan ~ packet
Q: How long until caravan is lined up before 2nd toll booth?
Time to “push” entire caravan through toll booth onto highway = 12*10 = 120 sec
Time for last car to propagate from 1st to 2nd toll both: 100km/(100km/hr)= 1 hr
A: 62 minutes
toll
booth
toll
booth
ten-car
caravan
100 km
100 km

## Slide 112: Caravan analogy (more)
Cars now “propagate” at 1000 km/hr
Toll booth now takes 1 min to service a car
Q: Will cars arrive to 2nd booth before all cars serviced at 1st booth?
Yes! After 7 min, 1st car at 2nd booth and 3 cars still at 1st booth.
1st bit of packet can arrive at 2nd router before packet is fully transmitted at 1st router!
toll
booth
toll
booth
ten-car
caravan
100 km
100 km

## Slide 113: Nodal delay
dproc = processing delay
  typically a few microsecs or less
dqueue = queuing delay
  depends on congestion
dtrans = transmission delay
  = L/R, significant for low-speed links
dprop = propagation delay
  a few microsecs to hundreds of msecs

## Slide 114: Queueing delay (revisited)
R=link bandwidth (bps)
L=packet length (bits)
a=average packet arrival rate
traffic intensity = La/R
La/R ~ 0: average queueing delay small
La/R -> 1: delays become large
La/R > 1: more “work” arriving than can be serviced, average delay infinite!
La/R ~ 0
La/R -> 1

## Slide 115: “Real” Internet delays and routes
What do “real” Internet delay & loss look like?
Traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
  sends three packets that will reach router i on path towards destination
  router i will return packets to sender
  sender times interval between transmission and reply.
3 probes
3 probes
3 probes

## Slide 116: “Real” Internet delays and routes
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
Three delay measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
* means no response (probe lost, router not replying)
trans-oceanic
link

## Slide 117: Packet loss
queue (aka buffer) preceding link in buffer has finite capacity
when packet arrives to full queue, packet is dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not retransmitted at all
A
B
packet being transmitted
packet arriving to
full buffer is lost
buffer
(waiting area)

## Slide 118: Throughput
throughput: rate (bits/time unit) at which bits transferred between sender/receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
Rs bits/sec)
pipe that can carry
fluid at rate
Rc bits/sec)

## Slide 119: Throughput (more)
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec

## Slide 120: Throughput: Internet scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck
Rs
Rs
Rs
Rc
Rc
Rc
R

## Slide 121
1. Protocol Layers
2. Why Layering？
3. ISO:OSI vs. TCP/IP 7:5
4. Internet Protocol Stack
5. PDUs of TCP/IP
6. TCP/IP Protocol Suite
  1.8 Protocol layers, service models

## Slide 122: What is a protocol?
protocols define format, order of msgs sent and received among network entities, and actions taken on msg transmission, receipt
Three factors of protocol
  语法
  语义
  同步
Notes: 语法：数据与控制信息的结构或格式；
语义：需要发出何种控制信息，完成动作及作出响应。
同步：事件实现顺序的详细说明。

## Slide 123: Protocol “Layers”
In order to ensure exactitude transmission, there are many affairs to deal with:
  send signals(信令) to active the link
  tell networks to find the receiver
  check if the receiver is standing by
  deal with different formats of data and message
  check errors when transmitting
  deal with delay and loss
  …

## Slide 124: Protocol “Layers”
Networks are complex!
many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question:
Is there any hope of organizing structure of network?
Or at least our discussion of networks?

## Slide 125: Organization of air travel
a series of steps
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing

## Slide 126: Layering of airline functionality
ticket (purchase)
baggage (check)
gates (load)
runway (takeoff)
airplane routing
departure
airport
arrival
airport
intermediate air-traffic
control centers
airplane routing
airplane routing
ticket (complain)
baggage (claim
gates (unload)
runway (land)
airplane routing
ticket
baggage
gate
takeoff/landing
airplane routing
Layers: each layer implements a service
  via its own internal-layer actions
  relying on services provided by layer below

## Slide 127: Layering of traditional mail system
Layer 4
Layer 3
Layer 2
Layer 1
Layers: each layer implements a service
  via its own internal-layer actions
  relying on services provided by layer below
Alice
Bob
Writing Reading
Encapsulation/Address
Delivery
Transport

## Slide 128: 两个主机交换文件
文件传送模块
主机 1
主机 2
文件传送模块
只看这两个文件传送模块
好像文件及文件传送命令
是按照水平方向的虚线传送的
把文件交给下层模块
进行发送
把收到的文件交给
上层模块

## Slide 129: 再设计一个通信服务模块
文件传送模块
主机 1
主机 2
文件传送模块
只看这两个通信服务模块
好像可直接把文件
可靠地传送到对方
把文件交给下层模块
进行发送
把收到的文件交给
上层模块
通信服务模块
通信服务模块

## Slide 130: 再设计一个网络接入模块
文件传送模块
主机 1
主机 2
文件传送模块
通信服务模块
通信服务模块
网络接入模块
网络接入模块
通信网络
网络
接口
网络
接口
网络接入模块负责做与网络接口细节有关的工作
例如，规定传输的帧格式，帧的最大长度等。

## Slide 131: Why layering?
分层可以带来的好处：
  各层之间是独立的，将问题分解为许多子问题
  灵活性好，一层的变化不会影响其他层
  机构上可以分割开
  易于实现和维护
  能够促进标准化工作
每一层要做的工作
  差错控制
  流量控制
  分段和重装
  复用和分用
  连接建立和连接释放
  …

## Slide 132: Why layering?
Dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system
layering considered harmful?

## Slide 133: ISO:OSI vs. TCP/IP
ISO: OSI/RM ( Open System Interconnection Reference Model, 开放系统互联基本参考模型)
  In order to interconnect different networks
  1977-1984: ISO 7489
  7 layers
  理论上的标准
应用层
会话层
表示层
传输层
网络层
数据链路层
物理层
为什么OSI没有得到广泛应用？

## Slide 134: ISO:OSI vs. TCP/IP
TCP/IP
  Driven by Industries
  From 1970’s up to now: the Heart of Internet
  5 layers
应用层
传输层
网络层
数据链路层
物理层

## Slide 135: Internet protocol stack
application: supporting network applications
  FTP, SMTP, HTTP,POP3
transport: host-host data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols,ICMP,IGMP,RIP
link: data transfer between neighboring network elements
  PPP, Ethernet
physical: bits “on the wire”
application
transport
network
link
physical

## Slide 136
局域网
广域网
HOST S1
HOST S2
Router1
Router2
RouterR3
电话网
局域网
主机 s1 向 s2 发送数据
链路层
应用层
运输层
网络层
物理层
链路层
应用层
运输层
网络层
物理层
链路层
网络层
物理层
链路层
网络层
物理层
链路层
网络层
物理层
R1
R2
R3
S1
S2
从层次上来看数据的流动

## Slide 137: Encapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame

## Slide 138: PDUs in TCP/IP
Application layer: Message (报文)
Transport layer: Datagram(数据报)/Segment(报文段)
Network Layer: Packet/Datagram(分组，数据包)
Data Link Layer: Frame(帧)
Physical Layer: bits “on the wire”
…
01010001100111…..

## Slide 139: TCP/IP protocol Suite
Suite: big family with many members.
Application Layer
Transport Layer
Internet Layer
Link Layer
HTTP
FTP
SMTP
DNS
RTP
TCP
UDP
…
…
IP
Network Interface 1
Network Interface 2
Network Interface 1
…
ICMP
IGMP
ARP

## Slide 140: 实体、协议、服务和服务访问点
实体(entity) 表示任何可发送或接收信息的硬件或软件进程。
协议是控制两个对等实体进行通信的规则的集合。
在协议的控制下，两个对等实体间的通信使得本层能够向上一层提供服务。
要实现本层协议，还需要使用下层所提供的服务。

## Slide 141
本层的服务用户只能看见服务而无法看见下面的协议。
下面的协议对上面的服务用户是透明的。
协议是“水平的”，即协议是控制对等实体之间通信的规则。
服务是“垂直的”，即服务是由下层向上层通过层间接口提供的。
同一系统相邻两层的实体进行交互的地方，称为服务访问点 SAP (Service Access Point)。

## Slide 142
协议(n + 1)
SAP
SAP
交换原语
交换原语
实体(n + 1)
服务提供者
第 n 层
第 n + 1 层
实体(n + 1)
服务用户
实体(n)
实体(n)
协议(n)

## Slide 143: 协议很复杂
协议必须把所有不利的条件事先都估计到，而不能假定一切都是正常的和非常理想的。
看一个计算机网络协议是否正确，不能光看在正常情况下是否正确，而且还必须非常仔细地检查这个协议能否应付各种异常情况。

## Slide 144: 著名的协议举例
占据东、西两个山顶的蓝军1和蓝军2与驻扎在山谷的白军作战。其力量对比是：单独的蓝军1或蓝军2打不过白军，但蓝军1和蓝军2协同作战则可战胜白军。现蓝军1拟于次日正午向白军发起攻击。于是用计算机发送电文给蓝军2。但通信线路很不好，电文出错或丢失的可能性较大（没有电话可使用）。因此要求收到电文的友军必须送回一个确认电文。但此确认电文也可能出错或丢失。试问能否设计出一种协议使得蓝军1和蓝军2能够实现协同作战因而一定（即100 %而不是99.999…%）取得胜利？

## Slide 145
明日正午进攻，如何？
同意
收到“同意”
收到：收到“同意”
…
…
…
…
…
…
这样的协议无法实现！

## Slide 146
  1.9 Network Security

## Slide 147: Network Security
The field of network security is about:
  how bad guys can attack computer networks
  how we can defend networks against attacks
  how to design architectures that are immune to attacks
Internet not originally designed with (much) security in mind
  original vision: “a group of mutually trusting users attached to a transparent network” 
  Internet protocol designers playing “catch-up”
  Security considerations in all layers!

## Slide 148: Bad guys can put malware into hosts via Internet
Malware can get in host from a virus, worm, or trojan horse.
Spyware malware can record keystrokes, web sites visited, upload info to collection site.
Infected host can be enrolled in a botnet, used for spam and DDoS attacks.
Malware is often self-replicating: from an infected host, seeks entry into other hosts

## Slide 149: Bad guys can put malware into hosts via Internet
Trojan horse
  Hidden part of some otherwise useful software
  Today often on a Web page (Active-X, plugin)
Virus
  infection by receiving object (e.g., e-mail attachment), actively executing
  self-replicating: propagate itself to other hosts, users
Worm:
  infection by passively receiving object that gets itself executed
  self- replicating: propagates to other hosts, users
Sapphire Worm: aggregate scans/sec
in first 5 minutes of outbreak (CAIDA, UWisc data)

## Slide 150: Bad guys can attack servers and network infrastructure
Denial of service (DoS): attackers make resources (server, bandwidth) unavailable to legitimate traffic by overwhelming resource with bogus traffic
select target
break into hosts around the network (see botnet)
send packets toward target from compromised hosts
target

## Slide 151: The bad guys can sniff packets
Packet sniffing:
  broadcast media (shared Ethernet, wireless)
  promiscuous network interface reads/records all packets (e.g., including passwords!) passing by
A
B
C
src:B dest:A payload
  Wireshark software used for end-of-chapter labs is a (free) packet-sniffer

## Slide 152: The bad guys can use false source addresses
IP spoofing: send packet with false source address
A
B
C
src:B dest:A payload

## Slide 153: The bad guys can record and playback
record-and-playback: sniff sensitive info (e.g., password), and use later
  password holder is that user from system point of view
A
B
C
src:B dest:A user: B; password: foo

## Slide 154: Introduction: Summary
Covered a “ton” of material!
Internet overview
what’s a protocol?
network edge, core, access network
  packet-switching versus circuit-switching
Internet/ISP structure
performance: loss, delay
layering and service models
History
Security
You now have:
context, overview, “feel” of networking
more depth, detail to follow!